## Slide 1: Computer Architecture (Fall 2021)
Instruction Set Principles
Dr. Yujuan Tan (谭玉娟)
Office: Main Building 0626
Email: tanyujuan@cqu.edu.cn
Lecture 8

## Slide 2: How Does a Machine Process Instructions?
What does processing an instruction mean?
Remember the von Neumann model
A = Architectural (programmer visible) state before an instruction is processed
Process instruction
A’ = Architectural (programmer visible) state after an instruction is processed
Processing an instruction: Transforming A to A’ according to the ISA specification of the instruction
Notes: 处理指令意味着什么？
还记得冯·诺依曼模型吗
A=指令处理前的架构（程序员可见）状态
过程指令
A’=指令处理后的体系结构（程序员可见）状态
处理指令：根据指令的ISA规范将A转换为A’

## Slide 3: The “Process instruction” Step
ISA specifies abstractly what A’ should be, given an instruction and A
  It defines an abstract finite state machine where
    State = programmer-visible state
    Next-state logic = instruction execution specification
  From ISA point of view, there are no “intermediate states” between A and A’ during instruction execution
    One state transition per instruction
Microarchitecture implements how A is transformed to A’
  There are many choices in implementation
  We can have programmer-invisible state to optimize the speed of instruction execution: multiple state transitions per instruction
    Choice 1: A  A’ (transform A to A’ in a single clock cycle)
    Choice 2: A  A+MS1  A+MS2  A+MS3  A’ (take multiple clock cycles to transform A to A’)
Notes: ISA抽象地指定了“A”应该是什么，给出了一条指令和一个
-它定义了一个抽象的有限状态机，其中
---状态=程序员可见状态
---下一状态逻辑=指令执行规范
-从ISA的角度来看，不存在“中间状态”
在指令执行期间在A和A之间
每个指令一个状态转换
微体系结构实现了如何将A转换为
在实现中有很多选择
我们可以让程序员看不见状态来优化指令执行速度：每条指令有多个状态转换
选择1：A A'（在单个时钟周期内将A转换为A）
选择2：A A+MS1 A+MS2 A+MS3 A'（采用多个时钟周期将A转换为A'）

## Slide 4: A Very Basic Instruction Processing Engine
Each instruction takes a single clock cycle to execute
Only combinational logic is used to implement instruction execution
  No intermediate, programmer-invisible state updates
A = Architectural (programmer visible) state
at the beginning of a clock cycle
Process instruction in one clock cycle
A’ = Architectural (programmer visible) state
at the end of a clock cycle
Notes: 每一条指令执行一个时钟周期
只有组合逻辑用于实现指令执行
---没有中间的、程序员不可见的状态更新
A=时钟周期开始时的架构（程序员可见）状态
在一个时钟周期内处理指令
A'=时钟周期结束时的体系结构（程序员可见）状态

## Slide 5: Remember: Programmer Visible (Architectural) State
M[0]
M[1]
M[2]
M[3]
M[4]
M[N-1]
Memory
array of storage locations
indexed by an address
Program Counter
memory address
of the current instruction
Registers
- given special names in the ISA
(as opposed to addresses)
- general vs. special purpose
Instructions (and programs) specify how to transform
the values of programmer visible state

## Slide 6: Single-cycle vs. Multi-cycle Machines
Single-cycle machines
  Each instruction takes a single clock cycle
  All state updates made at the end of an instruction’s execution
  Big disadvantage: The slowest instruction determines cycle time  long clock cycle time
Multi-cycle machines
  Instruction processing broken into multiple cycles/stages
  State updates can be made during an instruction’s execution
  Architectural state updates made only at the end of an instruction’s execution
  Advantage over single-cycle: The slowest “stage” determines cycle time
  Both single-cycle and multi-cycle machines literally follow the von Neumann model at the microarchitecture level
Notes: 单循环机器
--每条指令都有一个时钟周期
--在指令执行结束时进行的所有状态更新
--最大的缺点：最慢的指令决定了周期时间 长时钟周期时间
多周期机器
--分为多个周期/阶段的指令处理
--可以在指令执行期间进行状态更新
--仅在指令执行结束时进行的体系结构状态更新
--相对于单循环的优势：最慢的“阶段”决定循环时间
单周期和多周期机器实际上都遵循微体系结构级别的冯·诺依曼模型

## Slide 7: Instruction Processing “Cycle”
Instructions are processed under the direction of a “control unit” step by step.
Instruction cycle: Sequence of steps to process an instruction
Fundamentally, there are six phases:
Fetch
Decode
Evaluate Address
Fetch Operands
Execute
Store Result
Not all instructions require all six stages
Notes: 指令在“控制单元”的指导下逐步处理。
指令周期：处理指令的步骤顺序
基本上分为六个阶段：
取来
解码
评估地址
获取操作数
处决
存储结果
并非所有说明都需要全部六个阶段

## Slide 8: Instruction Processing “Cycle” vs. Machine Clock Cycle
Single-cycle machine:
  All six phases of the instruction processing cycle take a single machine clock cycle to complete
Multi-cycle machine:
  All six phases of the instruction processing cycle can take multiple machine clock cycles to complete
  In fact, each phase can take multiple clock cycles to complete
Notes: 单循环机器：
指令处理周期的所有六个阶段都需要一个机器时钟周期才能完成
多循环机器：
指令处理周期的所有六个阶段可能需要多个机器时钟周期才能完成
事实上，每个阶段可能需要多个时钟周期才能完成

## Slide 9: Instruction Processing Viewed Another Way
Instructions transform Data (A) to Data’ (A’)
This transformation is done by functional units
  Units that “operate” on data
These units need to be told what to do to the data
An instruction processing engine consists of two components
  Datapath: Consists of hardware elements that deal with and transform data signals
    functional units that operate on data
    hardware structures (e.g. wires and muxes) that enable the flow of data into the functional units and registers
    storage units that store data (e.g., registers)
  Control logic: Consists of hardware elements that determine control signals, i.e., signals that specify what the datapath elements should do to the data
Notes: 指令将数据（A）转换为数据“（A”）
这种转换是由功能单元完成的
--对数据进行“操作”的单元
需要告诉这些单位如何处理数据
指令处理引擎由两个组件组成
--数据路径：由处理和转换数据信号的硬件元素组成
----对数据进行操作的功能单元
----使数据能够流入功能单元和寄存器的硬件结构（如导线和多路复用器）
----存储数据的存储单元（如寄存器）
--控制逻辑：由确定控制信号的硬件元素组成，即指定datapath元素对数据应做什么的信号

## Slide 10: Single-cycle vs. Multi-cycle: Control & Data
Single-cycle machine:
  Control signals are generated in the same clock cycle as data signals are operated on
  Everything related to an instruction happens in one clock cycle
Multi-cycle machine:
  Control signals needed in the next cycle can be generated in the previous cycle
  Latency of control processing can be overlapped with latency of datapath operation
We will see the difference clearly in microprogrammed multi-cycle microarchitecture
Notes: 单循环机器：
--控制信号与数据信号在同一时钟周期内产生
--与指令相关的一切都发生在一个时钟周期内
多循环机器：
--下一个循环所需的控制信号可在上一个循环中产生
--控制处理的延迟可以与数据路径操作的延迟重叠
我们将清楚地看到微程序多周期微体系结构的区别

## Slide 11: Performance Analysis
Execution time of an instruction
  {CPI} x {clock cycle time}
Execution time of a program
  Sum over all instructions [{CPI} x {clock cycle time}]
  {# of instructions} x {Average CPI} x {clock cycle time}
Single cycle microarchitecture performance
  CPI = 1
  Clock cycle time = long
Multi-cycle microarchitecture performance
  CPI = different for each instruction
    Average CPI  hopefully small
  Clock cycle time = short
Notes: 指令的执行时间
{CPI}x{时钟周期时间}
程序的执行时间
--所有指令总和[{CPI}x{时钟周期时间}]
--{指令数}x{平均CPI}x{时钟周期时间}
单周期微体系结构性能
--消费物价指数=1
--时钟周期时间=长
多周期微体系结构性能
--CPI=每个指令的不同
----平均消费物价指数 希望很小
--时钟周期时间=短

## Slide 12: A Single Cycle Microarchitecture
Single-cycle machine
ANext
A
Sequential
Logic
(State)
Combinational
Logic

## Slide 13: Let’s Start with the State Elements
Data and control inputs

## Slide 14: For Now, We Will Assume
“Magic” memory and register file
Combinational read
  output of the read data port is a combinational function of the register file contents and the corresponding read select port
Synchronous write
  the selected register is updated on the positive edge clock transition when write enable is asserted
    Cannot affect read output in between clock edges
    Can affect read output at clock edges (but who cares?)
Single-cycle, synchronous memory
  Contrast this with memory that tells when the data is ready
  i.e., Ready bit: indicating the read or write is done
Notes: “魔术”内存和寄存器文件
组合读
--读取数据端口的输出是寄存器文件内容和相应读取选择端口的组合函数
同步写入
--当断言写启用时，所选寄存器在正边缘时钟转换时更新
----不能影响时钟边缘之间的读取输出
----会影响时钟边缘的读取输出（但谁在乎呢？）
单周期同步存储器
--将其与告诉数据何时准备好的内存进行对比
--i、 就绪位：表示读或写操作已完成

## Slide 15: Instruction Processing
5 generic steps
  Instruction fetch (IF)
  Instruction decode and register operand fetch (ID/RF)
  Execute/Evaluate memory address (EX/AG)
  Memory operand fetch (MEM)
  Store/writeback result (WB)
IF
ID/RF
EX/AG
MEM
WB
Notes: 5一般步骤
指令提取（IF）
指令解码和寄存器操作数提取（ID/RF）
执行/评估内存地址（EX/AG）
内存操作数提取（MEM）
存储/写回结果（WB）

## Slide 16: What Is To Come: The Full Datapath
PCSrc2=Br Taken
PCSrc1=Jump
ALU operation
bcond
JAL, JR, JALR omitted

## Slide 17: Single-Cycle Datapath for Arithmetic and Logical Instructions
Notes: 算术和逻辑指令的单周期数据路径

## Slide 18: R-Type ALU Instructions
Assembly (e.g., register-register signed addition)
ADD rdreg rsreg rtreg
Machine encoding
Semantics
if MEM[PC] == ADD rd rs rt
  GPR[rd]  GPR[rs] + GPR[rt]
  PC  PC + 4
0
6-bit
rs
5-bit
rt
5-bit
R-type
rd
5-bit
0
5-bit
ADD
6-bit

## Slide 19: ALU Datapath
1
15:11
20:16
25:21
**Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]
if MEM[PC] == ADD rd rs rt
  GPR[rd]  GPR[rs] + GPR[rt]
  PC  PC + 4
Combinational
state update logic
IF
ID
EX
MEM
WB

## Slide 20: I-Type ALU Instructions
Assembly (e.g., register-immediate signed additions)
ADDI rtreg rsreg immediate16
Machine encoding
Semantics
if MEM[PC] == ADDI rt rs immediate
GPR[rt]  GPR[rs] + sign-extend (immediate)
PC  PC + 4
ADDI
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type

## Slide 21: Datapath for R and I-Type ALU Insts.
1
ALUSrc
isItype
RegDest
isItype
15:11
20:16
25:21
if MEM[PC] == ADDI rt rs immediate
  GPR[rt]  GPR[rs] + sign-extend (immediate)
  PC  PC + 4
Combinational
state update logic
IF
ID
EX
MEM
WB

## Slide 22: Single-Cycle Datapath for Data Movement Instructions
Notes: 用于数据移动指令的单周期数据路径

## Slide 23: Load Instructions
Assembly (e.g., load 4-byte word)
LW rtreg offset16 (basereg)
Machine encoding
Semantics
if MEM[PC]==LW rt offset16 (base)
    EA = sign-extend(offset) + GPR[base]
    GPR[rt]  MEM[ translate(EA) ]
    PC  PC + 4
LW
6-bit
base
5-bit
rt
5-bit
offset
16-bit
I-type

## Slide 24: LW Datapath
ALUSrc
if MEM[PC]==LW rt offset16 (base)
EA = sign-extend(offset) + GPR[base]
GPR[rt]  MEM[ translate(EA) ]
PC  PC + 4
Combinational
state update logic
IF
ID
EX
MEM
WB
1
add
isItype
RegDest
isItype

## Slide 25: Store Instructions
Assembly (e.g., store 4-byte word)
SW rtreg offset16 (basereg)
Machine encoding
Semantics
if MEM[PC]==SW rt offset16 (base)
    EA = sign-extend(offset) + GPR[base]
    MEM[ translate(EA) ]  GPR[rt]
    PC  PC + 4
SW
6-bit
base
5-bit
rt
5-bit
offset
16-bit
I-type

## Slide 26: SW Datapath
if MEM[PC]==SW rt offset16 (base)
EA = sign-extend(offset) + GPR[base]
MEM[ translate(EA) ]  GPR[rt]
PC  PC + 4
Combinational
state update logic
IF
ID
EX
MEM
WB
0
add
ALUSrc
isItype
RegDest
isItype

## Slide 27: Load-Store Datapath
!isStore
add
isStore
isLoad
ALUSrc
isItype
RegDest
isItype

## Slide 28: Datapath for Non-Control-Flow Insts.
!isStore
isStore
isLoad
ALUSrc
isItype
MemtoReg
isLoad
RegDest
isItype

## Slide 29: Single-Cycle Datapath for Control Flow Instructions
Notes: 控制流指令的单周期数据路径

## Slide 30: Unconditional Jump Instructions
Assembly
J immediate26
Machine encoding
Semantics
if MEM[PC]==J immediate26
  target = { PC[31:28], immediate26, 2’b00 }
  PC  target
J
6-bit
immediate
26-bit
J-type

## Slide 31: Unconditional Jump Datapath
ALUSrc
concat
PCSrc
isJ
What about JR, JAL, JALR?
?
0
X
0
0
X
if MEM[PC]==J immediate26
PC = { PC[31:28], immediate26, 2’b00 }

## Slide 32: Conditional Branch Instructions
Assembly (e.g., branch if equal)
BEQ rsreg rtreg immediate16
Machine encoding
Semantics (assuming no branch delay slot)
if MEM[PC]==BEQ rs rt immediate16
    target = PC + 4 + sign-extend(immediate) x 4
    if GPR[rs]==GPR[rt] then PC  target
    else PC  PC + 4
BEQ
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type

## Slide 33: Conditional Branch Datapath (For You to Fix)
PCSrc
concat
0
sub
bcond
watch out

## Slide 34: Putting It All Together
PCSrc2=Br Taken
PCSrc1=Jump
ALU operation
bcond
JAL, JR, JALR omitted