## Slide 1: Computer Architecture (Fall 2021)
Pipelining
Dr. Yujuan Tan (谭玉娟)
Office: Main Building 0626
Email: tanyujuan@cqu.edu.cn
Lecture 9

## Slide 2: Can We Do Better?
What limitations do you see with the multi-cycle design?
Limited concurrency
  Some hardware resources are idle during different phases of instruction processing cycle
  “Fetch” logic is idle when an instruction is being “decoded” or “executed”
  Most of the datapath is idle when a memory access is happening

## Slide 3: Can We Use the Idle Hardware to Improve Concurrency?
Goal: Concurrency  throughput (more “work” completed in one cycle)
Idea: When an instruction is using some resources in its processing phase, process other instructions on idle resources not needed by that instruction
  E.g., when an instruction is being decoded, fetch the next instruction
  E.g., when an instruction is being executed, decode another instruction
  E.g., when an instruction is accessing data memory (ld/st), execute the next instruction
  E.g., when an instruction is writing its result into the register file, access data memory for the next instruction

## Slide 4: Pipelining: Basic Idea
More systematically:
  Pipeline the execution of multiple instructions
  Analogy: “Assembly line processing” of instructions
Idea:
  Divide the instruction processing cycle into distinct “stages” of processing
  Ensure there are enough hardware resources to process one instruction in each stage
  Process a different instruction in each stage
    Instructions consecutive in program order are processed in consecutive stages
Benefit: Increases instruction processing throughput (1/CPI)
Downside: Start thinking about this…

## Slide 5: The Laundry Analogy
“place one dirty load of clothes in the washer”
“when the washer is finished, place the wet load in the dryer”
“when the dryer is finished, take out the dry load and fold”
“when folding is finished, ask your roommate (??) to put the clothes away”
- steps to do a load are sequentially dependent
- no dependence between different loads
- different steps do not share resources

## Slide 6: Pipelining Multiple Loads of Laundry
- latency per load is the same
- throughput increased by 4
- 4 loads of laundry in parallel
- no additional resources

## Slide 7: Pipelining Multiple Loads of Laundry: In Practice
the slowest step decides throughput

## Slide 8: Pipelining Multiple Loads of Laundry: In Practice
A
B
A
B
Throughput restored (2 loads per hour) using 2 dryers

## Slide 9: An Ideal Pipeline
Goal: Increase throughput with little increase in cost (hardware cost, in case of instruction processing)
Repetition of identical operations
  The same operation is repeated on a large number of different inputs
Repetition of independent operations
  No dependencies between repeated operations
Uniformly partitionable suboperations
  Processing can be evenly divided into uniform-latency suboperations (that do not share resources)
Fitting examples: automobile assembly line, doing laundry
  What about the instruction processing “cycle”?

## Slide 10: Ideal Pipelining
combinational logic (F,D,E,M,W)
T psec
BW=~(1/T)
BW=~(2/T)
T/2 ps (F,D,E)
T/2 ps (M,W)
BW=~(3/T)
T/3
ps (F,D)
T/3
ps (E,M)
T/3
ps (M,W)

## Slide 11: More Realistic Pipeline: Throughput
Nonpipelined version with delay T
BW = 1/(T+S) where S = latch delay
k-stage pipelined version
BWk-stage = 1 / (T/k +S )
BWmax = 1 / (1 gate delay + S )
T ps
T/k
ps
T/k
ps

## Slide 12: More Realistic Pipeline: Cost
Nonpipelined version with combinational cost G
Cost = G+L where L = latch cost
k-stage pipelined version
Costk-stage = G + Lk
G gates
G/k
G/k

## Slide 13: Pipelining Instruction Processing

## Slide 14: Remember: The Instruction Processing Cycle
  Fetch
  Decode
  Evaluate Address
  Fetch Operands
  Execute
  Store Result
  1. Instruction fetch (IF)
  2. Instruction decode and
  register operand fetch (ID/RF)
  3. Execute/Evaluate memory address (EX/AG)
  4. Memory operand fetch (MEM)
  5. Store/writeback result (WB)

## Slide 15: Remember the Single-Cycle Uarch
PCSrc2=Br Taken
PCSrc1=Jump
ALU operation
bcond
T
BW=~(1/T)

## Slide 16: Dividing Into Stages
200ps
Is this the correct partitioning?
Why not 4 or 6 stages? Why not different boundaries?
100ps
200ps
200ps
100ps
RF
write
ignore
for now

## Slide 17: Instruction Pipeline Throughput
800ps
800ps
800ps
200ps
200ps
200ps
200ps
200ps
200ps
200ps
5-stage speedup is 4, not 5 as predicated by the ideal model. Why?

## Slide 18: Enabling Pipelined Processing: Pipeline Registers
T
No resource is used by more than 1 stage!
IRD
PCF
PCD+4
PCE+4
nPCM
AE
BE
ImmE
AoutM
BM
MDRW
AoutW
T/k
ps
T/k
ps

## Slide 19: Pipelined Operation Example
All instruction classes must follow the same path and timing
through the pipeline stages. Any performance impact?

## Slide 20: Pipelined Operation Example

## Slide 21: Illustrating Pipeline Operation: Operation View
MEM
EX
ID
IF
Inst4
WB
IF
MEM
IF
MEM
EX
t0
t1
t2
t3
t4
t5
ID
EX
IF
ID
IF
ID
Inst0
ID
IF
Inst1
EX
ID
IF
Inst2
MEM
EX
ID
IF
Inst3
WB
WB
MEM
EX
WB

## Slide 22: Illustrating Pipeline Operation: Resource View
I0
I0
I1
I0
I1
I2
I0
I1
I2
I3
I0
I1
I2
I3
I4
I1
I2
I3
I4
I5
I2
I3
I4
I5
I6
I3
I4
I5
I6
I7
I4
I5
I6
I7
I8
I5
I6
I7
I8
I9
I6
I7
I8
I9
I10
 | t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9 | t10
IF |  |  |  |  |  |  |  |  |  |  | 
ID |  |  |  |  |  |  |  |  |  |  | 
EX |  |  |  |  |  |  |  |  |  |  | 
MEM |  |  |  |  |  |  |  |  |  |  | 
WB |  |  |  |  |  |  |  |  |  |  | 

## Slide 23: Pipelining Lessons
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup

## Slide 24
Other Definitions
Pipe stage or pipe segment
  A decomposable unit of the fetch-decode-execute paradigm
Pipeline depth
  Number of stages in a pipeline
Machine cycle
  Clock cycle time
Latch
  Per phase/stage local information storage unit

## Slide 25
Design Issues
Balance the length of each pipeline stage
Problems
  Usually, stages are not balanced
  Pipelining overhead
  Hazards (conflicts)
Performance (throughput CPU performance equation)
  Decrease of the CPI
  Decrease of cycle time
Throughput =
Time per instruction on unpipelined machine
Depth of the pipeline

## Slide 26
1st and 2nd Instruction cycles
Instruction fetch (IF)
  IR Mem[PC];
  NPC PC + 4
Instruction decode & register fetch (ID)
  A Regs[IR6..10];
  B Regs[IR11..15];
  Imm ((IR16)16 # # IR16..31)

## Slide 27
3rd Instruction cycle
Execution & effective address (EX)
  Memory reference
    ALUOutput A + Imm
  Register - Register ALU instruction
    ALUOutput A func B
  Register - Immediate ALU instruction
    ALUOutput A op Imm
  Branch
    ALUOutput NPC + Imm; Cond (A op 0)

## Slide 28
4th Instruction cycle
Memory access & branch completion (MEM)
  Memory reference
    PC NPC
    LMD Mem[ALUOutput] (load)
    Mem[ALUOutput] B (store)
  Branch
    if (cond) PC ALUOutput; else PC NPC

## Slide 29
5th Instruction cycle
Write-back (WB)
  Register - register ALU instruction
    Regs[IR16..20] ALUOutput
  Register - immediate ALU instruction
    Regs[IR11..15] ALUOutput
  Load instruction
    Regs[IR11..15] LMD

## Slide 30
Simple Implementation of a MIPS
• temporary registers
•hold values between clock cycles for an instruction
• state elements (“visible part of the state”)
•hold values between successive instructions
• control logic (FSM or microcode controller)
• (not illustrated in the diagram above)

## Slide 31
MIPS Pipeline Implementation
• Apparently easy
– each clock
cycle becomes
a pipe stage
– temporary
registers
become pipe
registers
– new instruction
issued at each
clock cycle
• Result propagation
– register value to
be stored is
read during ID
and used in MEM
– ALU result
computed during
EX (or loaded
during MEM) and
store in WB
• pipeline registers
• hold values between clock cycles for an instruction
• prevent interference (edge-triggered flip-flops)
• state elements (“visible part of the state”)
• hold values between successive instructions

## Slide 32
MIPS Pipeline Implementation

## Slide 33
Multiple-Clock Cycle Pipeline Diagram
lw R10, 20(R1)
sub R11, R2, R3
add R12, R3, R4
lw R13, 24(R1)
add R14, R5, R6
Unlike some other speedup techniques, pipelining is fundamentally transparent to the programmer